## Slide 1: SIGNAL PROCESSING MONSOON PROJECT
GRP NAME:- SP DESIGNERS
YASH NITIN DUSANE(2022102078)
MANAS SACHIN DESHMUKH(2022102040)
ARYAMAN MAHAJAN(2022102034)

## Slide 2: WHAT IS AN ECHO?
Q1) Part 1 - Echo creation:-
“ECHO" refers to a delayed and attenuated version of a sound or
signal that is heard after the original sound. It is a time-delayed replication of the original signal,
where the delayed version is often quieter than the original due to the signal being reflected off
surfaces or travelling a longer path

## Slide 3: ECHO VERSUS ORIGINAL SIGNAL
An echo is a reflection of sound that arrives at the listener after bouncing off a surface. When comparing an original sound signal to its echo, there are several properties that can be different:
Time Delay:
  Original Signal: The sound is emitted and reaches the listener directly.
  Echo Signal: The sound reflects off a surface and then reaches the listener. There is a delay between the original signal and the echo, which is known as the echo delay or time delay.
Amplitude:
  Original Signal: The initial amplitude of the sound.
  Echo Signal: The amplitude of the echo can be different from the original signal. It may be weaker due to absorption by the reflecting surface or air, or it could be stronger if there's an amplifying surface.
Frequency Response:
  Original Signal: The frequency content of the original sound.
  Echo Signal: The frequency response of the echo may differ due to absorption of certain frequencies by the reflecting surface. High-frequency components may be attenuated more than low-frequency components

## Slide 4: ECHO VERSUS ORIGINAL SIGNAL
Number of Reflections:
Original Signal: There is only one source of sound.
Echo Signal: Depending on the environment, there may be multiple reflections, leading to multiple echoes. These subsequent reflections may be weaker and occur at later time intervals
Phase Distortion:
Original Signal: Phase information is usually preserved.
Echo Signal: Reflections may introduce phase distortions, especially if there are multiple reflections or complex surfaces involved. This can impact the stereo image and spatial perception

## Slide 5: PROBLEM INTRODUCTION AND APPROACH
Our task is to apply signal processing techniques to create an echo effect for the given
audio.
The echo effect should be audible but not overpowering, simulating a natural echo
found in acoustic environments
CONSIDER THE GIVEN INPUT AS X[N] THEN WE NEED TO ADD N ECHOES WITH DELAYS TO GET Y[N] , SO WE HAVE A DELAY ‘D’ BETWEEN THE SIGNALS SO WE WILL FIRST DESIGN AN IMPULSE RESPONSE H[N] WITH DECAYING MAGNITUDE 1,0.5,0.25 …..A GP WITH COMMON RATIO 0.5 WITH DELAY D BETWEEN TWO VALUES.

## Slide 6: APPROACH (CONTINUED)
NOW CONSIDER A SYSTEM WITH IMPULSE RESPONSE H[N] AND INPUT X[N] SO OUTPUT Y[N]=X[N]*H[N] (CONVOLUTION) .DUE TO DECAYING MAGNITUDE OF H[N] WHEN CONVOLVED WITH X[N] WE GET ECHOED VERSION OF X[N] WITH D DELAY

## Slide 7: MATLAB SCRIPT FOR THIS APPROACH
clc, clearvarsaudiofile = {"D:\DSP\Course_Project\Sample Audio Files\q1.wav";
"D:\DSP\Course_Project\Sample Audio Files\q1_hard.wav"};
[x,Fs] = audioread(audiofile{k});
a = 0.5;
n = 3;
x = transpose(x);
l = length(x);
d = -l/1.5;
h = zeros(1,n*(l+d)+1);
for k = 0:n-1,
h(k*(l+d)+1) = a^k;
endy = conv(x(1,:),h);plot(1:length(y),y)
%sound(y,Fs)end

## Slide 8: PROBLEM 2 INTRODUCTION AND APPROACH
Part 2 - Cancel the echo
In this section, you will be presented with an audio signal containing an echo with non-uniform
delays. Your task is to implement an echo cancellation algorithm to remove the echo components
from the signal, leaving only the original, clean audio.
APPROACH: GIVEN DESIRED SIGNAL USED OF LMS(LEAST MEAN SQUARE) METHOD WITH THE HELP OF THE CONCEPT OF ADAPTIVE FILTERS.

## Slide 9: THE LMS APPROACH
The Least Mean Squares (LMS) algorithm is a widely used adaptive filter algorithm in the field of digital signal processing. Adaptive filters are systems that can automatically adjust their parameters based on the input signals to optimize some criteria. The LMS algorithm is particularly popular for applications such as noise cancellation, system identification, and equalization

## Slide 10: LMS ALGORITHM
For a ﬁlter as shown in the ﬁgure the output
y(n) is given by
y(n) = w0x(n) + w1x(n ­ 1) + · · · + wpx(n ­ N )
= wT x(n)
as w and x(n) are both column vectors and to produce required result we need transpose of w
Now we consider as system as
shown where we want y(n) to be
an estimate of a target signal
d(n)
If x(n) is stationary then y(n) is
also stationary. x(n) and d(n) will
be jointly stationary.

## Slide 11: LMS ALGORITHM(CONTUINUED)
Taking autocorrelation we get RXX = E[x(n) xT (n)] = R
Taking cross-correlation we get P a column vector such that P = E[d(n)x(n)]
We need to minimize e(n) to ensure y(n) is a close estimate of d(n) . Taking mean squared error or expected value of e2(n)
E[e2(n)] = E[ (d(n) ­ wT x(n)) (d(n) ­ wT x(n))T ] substituting y(n) as wT x(n)
E[e2(n)] = E[d2(n)] ­ 2E[wT x(n) d(n)] + E[wT x(n) xT (n) w ]
Using properties of expectation and substituting cross correlation and autocorrelation
E[e2(n)] = E[d2(n)] ­ 2wT P + wT Rw
Taking gradient of this vector we get

## Slide 12: LMS ALGORITHM(CONTINUED)
∇wE[e2(n)] = 0 ­ 2∇wA + ∇wB
Here,
where A and B are
wT P
and wT Rw
where,
A = wT P
= w0P (0) · · · +
wk P (k)
+ · · · +
wN P (N )
δA δwk
= P (k)